TECHNICAL REPORT FSUTMS Transit Model Template Application Guide

Prepared for Florida Department of Transportation

December 2009

TECHNICAL REPORT

FSUTMS Transit Model Template Application Guide

Prepared for

Florida Department of Transportation

Prepared by

AECOM

300 E. Broad St, Suite 300

Columbus, OH- 43215

December 2009

CONTENTS

Executive Summary	1

CHAPTER 1: Importing the Transit model template	2

CHAPTER 2: Model Procedure	7

2.1	Compatibility Module	7

2.2	Transit Prep Module	8

2.3	Transit Paths Module	10

2.4	Mode Choice Module	11

2.5	Transit Assignment Module	13

2.6	Transit Reporting Module	14

CHAPTER 3: Catalog keys, input and output files	15

3.1	Catalog Keys	15

3.2	Input files	16

3.2.1	Highway networks	16

3.2.2	Highway skim files	17

3.2.3	Production trip rate file (GRATES)	18

3.2.4	Dwelling unit weights file (DUWEIGHTS)	18

3.2.5	Person trip file (PSNTRIPS_{Alt}{Year}.MAT)	18

3.2.6	Zonal data files	19

3.2.7	Transit line file (TROUTE_{year}{alt}.LIN)	19

3.2.8	System file (TSYSD.pts)	20

3.2.9	Fares file (TFAREStp_{year}{alt}.FAR)	21

3.2.10	Transit Coefficients file (TRN_COEFFICIENTS.DBF)	22

3.2.11	Mode Choice constants file (MC_CONSTANTS.DBF )	23

3.2.12	Percent walk file (PCWALK_{Year}{Alt}.DAT)	24

3.2.13	Mode choice targets (MC_TARGETS.DBF)	25

3.3	Key output files	27

3.3.1	Highway Vehicle Trip Table (HWYTTAB_{Alt}{Year}.MAT)	27

3.3.2	Person Trip Table (MODEOUT.MAT)	27

3.3.3	Transit assignment summary report (TASUM_{ALT}{YEAR}.PRN)	27

3.3.4	Transit Assignment Route-Level Report (TASROUTE_{ALT}{YEAR}.PRN)	28

3.3.5	Station Activity Report (Stations_{Alt}{Year}.prn)	30

CHAPTER 4: Changes in scripts	32

4.1	Compatibility Module Scripts	32

4.2	TPNET00C.S  (Transit speed for peak period)	32

4.3	TPNET00C.S (Transit speed for offpeak period)	33

4.4	TPPTR00A.S (Build peak access connectors)	33

4.5	TPPTR00B.S (Build offpeak access connectors)	33

4.6	TRPTR00A.S (Walk-Access Paths/Skims – peak)	33

4.7	TRPTR00B.S (Auto-Access Paths/Skims – peak)	34

4.8	TRPTR00C.S (Walk-Access Paths/Skims – offpeak)	34

4.9	TRPTR00D.S (Auto-Access Paths/Skims – offpeak)	34

4.10	MCPREP.S (Auto ownership percentage by TAZ for work and non-work purposes)	34

4.11	MCPREP.S and MCMAT00B.S	36

Appendix: Transit Model Tier A Template Screenshots	37

LIST OF FIGURES

FIGURE1: Transit model template	2

Figure 2: New Application Directory	3

Figure 3: New Application Directory Dialog Box	3

Figure 4: New Application Directory Dialog Box II	4

Figure 5: New Application Directory Dialog Box III	4

Figure 6: Insert Application Group	4

Figure 7: Transit model template in Olympus Training Model	6

Figure 8: Compatibility Module	8

Figure 9: Transit Prep Module	10

Figure 10: Transit Paths Module	11

Figure 11: Mode Choice Module	12

Figure 12: Transit Assignment Module	13

Figure 13: Transit Reporting Module	14

Figure 14: Transit Assignment Summary Report (Snippet)	28

Figure 15: Transit Assignment Route- Level Report (Snippet)	29

Figure 16: Station Activity Report (Snippet)	30

Figure 17: Transit Prep Module	38

Figure 18: Transit Paths Module	39

Figure 19: Mode Choice Module	40

Figure 20: Transit Assignment Module	41

Figure 21: Transit Reporting Module	42

LIST OF TABLES

Table 1: Output Files from the Highway Model Required by the Transit model template	5

Table 2: Files Required by the Transit Model	5

Table 3: Catalog Keys	15

Table 4: Highway Network Link Variables	16

Table 5: Highway Network Node Variables	17

Table 6: Highway skim tables for AUTOCON program	17

Table 7: Highway skim tables for mode choice module	18

Table 8: Columns in the GRATES File	18

Table 9: Columns in the DUWEIGHTS File	18

Table 10: Required fields in zonal data files	19

Table 11: Keywords to LINE Control Statement and Their Recommended Values	20

Table 12: Sub-keywords to Keyword N in LINE Control Statement	20

Table 13: Default Modes and Mode Numbers in SYSTEM.PTS File	21

Table 14: Default Operators, Operator Numbers, and FareSystems in TSYSD.PTS File	21

Table 15: Keywords to FARESYSTEM Control Statement and Their Recommended Values	22

Table 16: Default Fares Used In the Fares File	22

Table 17: Default Transfer Fares Used In the Fares File	22

Table 18: Default Transit Coefficients for Tier B/C	23

Table 19: Default Mode Choice Constants for Tier B/C	24

Table 20: Percent Walk File Format	24

Table 21: Default Mode Share Targets for Tier B/C	26

Table 22: Tables in the vehicle trip tables	27

Table 23: Transit Assignment Summary Report Format	28

Table 24: Transit Assignment Route-Level Report Format	29

# Executive Summary

The Florida Department of Transportation updated the standards for transit modeling in Cube Voyager in 2006. A CUBE Voyager transit model template (TMT) is being developed that incorporates these updated standards. This document provides the instructions for importing the TMT into a travel demand model (Chapter 1), descriptions of the model procedure (Chapter 2), the catalog keys, input and output files of the TMT (Chapter 3), and the scripts that must be modified by the user to customize the template to fit the model at hand (Chapter 4).

Just like a travel demand model, the transit model template must be calibrated and validated with observed data. The data required to calibrate and validate the TMT includes:

- Appropriate zonal area and connections to the highway network (zones larger than one square mile may not be able to connect to transit);

- Reasonable estimates of person travel patterns, which can be verified by using the Census Transportation Planning Package 2000 (work trips only) or other relatively large-sampled surveys;

- Reliable estimates of auto and transit travel times, which could be gathered from car probes, data from freeway management centers, automatic vehicle locators (AVLs) and public transit time tables;

- Observed linked transit trips by trip purpose, access mode, market segments and potentially by other dimensions, which can be developed via a transit on-board survey; and

- Boardings by route and potentially by other dimensions, which could be gathered from ridecheck (on/off) surveys, automated passenger counters (APCs) or fare collections.

The following steps must be followed in order to properly import and modify the TMT in a travel demand model:

- Import the template to the travel demand model (refer to Chapter 1),

- Review the modules within the template (Chapter 2),

- Connect input and output files from the model to the files in the template (Chapter 3),

- Modify the appropriate scripts and input files (Chapter 4),

- For the best year, calibrate the auto and transit speeds (or travel times) and compare them against observed data,

- Calibrate the mode choice model for the base year,

- Validate the base year transit assignments by comparing them to observed counts, and

- Test the template against at least one future alternative to assess its forecasting ability.

# CHAPTER 1: Importing the Transit model template

This chapter explains the procedures for importing the transit model template into the user’s travel demand model. The formats of the input and output files, the required fields for the input files, and the detailed description of the logic of the different groups of applications are noted in the subsequent chapters. The TMT can be downloaded from http://www.fsutmsonline.net/images/uploads/mtf-files/TransitApp.zip. Separate template has been developed for Tier A (cities with very “modest” transit service) and Tier B/C (cities with “intermediate” transit service) cities. The screenshot of the template for Tier B/C is shown in Figure 1 below.

FIGURE1: Transit model template

The TMT is used to prepare the transit network from the highway network, generate transit access connectors, transit skims and paths, obtain the shares and vehicle trips of all the modes/paths (both auto and transit) from the person trip table, assign the transit trips to transit service routes and produce transit assignment reports (summary, route-level, and station level reports). So, the transit model should be placed after the trip distribution step and before the highway assignment step.

The following steps must be followed to insert the template into a model:

- Open the transit model template in CUBE Voyager

  - Open TRANSITMODEL.app file from the applications\ folder. The screenshot of the application is shown in Figure 1.

- Create a new directory for this application and save it in the applications folder of the model

  - Go to ‘Application’ Tab and click on ‘New Application Directory’ (see the screenshot below).

Figure 2: New Application Directory

  - A dialog box as shown will appear. Click Ok.

Figure 3: New Application Directory Dialog Box

  - In the “choose directory” dialog box that follows, select the applications folder of the model., The initial folder points to the folder where the current TRANSITMODEL.app file is.

  - A dialog box as shown will appear. Click “Yes”.

Figure 4: New Application Directory Dialog Box II

  - A message will pop up saying “the project has program files that contains @...@ and %...%, file names cannot be copied.”. Click OK.

Figure 5: New Application Directory Dialog Box III

  - Close the application.

- Open the model into which transit model template needs to be imported:

  - Choose Group tab and Click on ‘Insert Application Group’ (screenshot is shown below).

Figure 6: Insert Application Group

  - Select TRANSITMODEL.app from the list. This will insert the TRANSITMODEL subgroup into the model.

  - Change the execution order of this step so that it is run after the trip distribution step. Execution order can be changed by right-clicking on the subgroup.

  - Link the input and output files from the transit model template to the files in other steps. The files input to the TMT are shown with the boxes on the left section of the template and all the output files are shown on the right section. This can be done by dragging and dropping the appropriate files that need to be connected from other steps to the location of the files in transit model template. Similarly, the output files of the template that need to be connected to the subsequent steps can be dragged and dropped.

The files that the template requires from the highway model are shown in Table 1. These files should be linked using the drag and drop method in Application Manager. The formats of these files are described in Chapter 3.

Table 1: Output Files from the Highway Model Required by the Transit model template

| File | Default File Name | Folder |
| --- | --- | --- |
| Unloaded highway network | UNLOADED_{alt}{year}.NET | Output |
| Pre-assigned highway network | PREASSGN_{alt}{year}.NET | Output |
| Person trip table | PSNTRIPS_{alt}{year}.MAT | Output |
| External-external vehicle trip table | EETABLE_{alt}{year}.MAT | Output |
| Congested auto skims | CONGSKIM_{alt}{year}.MAT | Output |
| Free flow auto skims | FREESKIM_{alt}{year}.MAT | Output |
| Production trip rates file | GRATES_MC.DBF | Input/Output |
| Dwelling units weight file | DUWEIGHTS.DBF | Input/Output |

Apart from the files mentioned in Table 1, the template also requires congested and free flow highway skim files that are used by the AUTOCON program. These files are read in directly by the program and they need not be linked to the highway model. These default file names are FHSKIMTT_{Alt}{Year}.MAT and RHSKIMTT_{Alt}{Year}.MAT.

Table 2 lists the input files that are not generated within the model and are used by the transit model template. These files are created before setting up the model. The default file names that have been used in the template are shown in bracket. The formats of these files are described in Chapter 3.

Table 2: Files Required by the Transit Model

| File | Default File Name | Folder |
| --- | --- | --- |
| Zonal Data File | ZONEDATA_{year}{alt}.DBF | Input |
| Transit Line File | TROUTE_{year}{alt}.LIN | Input |
| System Data File | TSYSD.PTS | Parameters |
| Fares File | TFARES.FAR | Parameters |
| All Walk Factors file | AllWalk.FAC | Parameters |
| Transit Coefficient File | TRN_COEFFICIENT.DBF | Parameter |
| Mode Choice Constant file | MC_CONSTANTS.DBF | Parameters |
| Station list file | STATREP_{year}{alt}.DAT | Input |

  - Follow the instructions mentioned in Readme.txt file present in the model folder to install the AUTOCON program.

  - Refer to Chapter 3 for a detailed account of the formats, required fields, and naming conventions of the input files. All the input files must be consistent with the formats and names mentioned in Chapter 3. The user may have to add some steps to change either the formats or the names of the files before connecting them to the transit model template.

  - Revise the values of the catalog keys in the Keys section of the model catalog. The list of keys that the template requires is mentioned in Chapter 3.

  - The transit model template is now imported into the model.

Step 4 of the Olympus model is the transit model template. The transit model template, when imported into the user’s model, should look like the screenshot.

Figure 7: Transit model template in Olympus Training Model

# CHAPTER 2: Model Procedure

The transit model template consists of six modules. In the Compatibility module, the highway model output files are made compatible with the TMT file formats. In the Transit Prep module, the factors files are created and the speeds of various transit modes are assigned. Next, access connectors are built and adjustments are made to walk access connectors. In the Transit Paths module, paths and skims are built. This is followed by path conditioning to eliminate certain paths from evaluation. The modal choice model is scripted in the Mode Choice Model module. A calibration routine has been set up in this module to calibrate the mode choice model to observed data specific to the modeling area. Transit trip tables are loaded onto the transit paths in the Transit Assignment module. In the Transit Reporting module, transit assignment summary reports are generated. A station report that notes the activity at selected stations is also produced. However, if the {BaseYearTransit} catalog key is set to 0, indicating the absence of transit for the base year, the TMT runs in a special mode where the TransitPrep, Transit Paths, Transit Assignment and Transit Reporting modules are bypassed and a highway only mode choice model is run.

Each of these modules is discussed in detail in this section. The Tier B/C template screenshots are presented in this chapter and the Tier A template screenshots are presented in the Appendix.

## Compatibility Module

The Compatibility module is shown in Figure 8. This module provides a central location for the user to modify/reorganize the output files from the highway module so that they are compatible with the format that the transit model template expects. A simple example of such a modification is the case where the person trip table from the highway model contains table name ‘HBNW’ for home-based non-work purpose trips. TMT expects this table name to be ‘HBO’ (as mentioned in Section 3.2.5). The compatibility module can be used to change this table name from ‘HBNW’ TO ‘HBO’. As shown in Figure 8, the module contains steps for changing each of the input files and must used only where necessary. The script files for all the steps are empty and the execution order of all the steps is set to 0 (will not execute in a model run). The user has to write the scripts and change the execution orders of the steps (to a number greater than 0) to run these steps in a model run. The output files from the steps in the module (which will be compatible with TMT) will have different filenames from the input files. However, the TMT expects the filenames to be same as those mentioned in Section 3.2. The pilot statement in the module can be used to copy the new files (that are now compatible with TMT) to those mentioned in Section 3.2.

Figure 8: Compatibility Module

## Transit Prep Module

The Transit Prep module is shown in Figure 9. This module runs only if there is transit service present in the alternative as indicated by {BaseYearTransit} catalog key set to 1.This module is divided into four groups of steps. In the first group (TrModelCheck), the existence and compatibility of the TMT input files are checked. The model run crashes if any of the input files are missing and an error message indicating the missing file is displayed on the task monitor of the run. In the second group, the TRANSIT.MAS file is created. Next, four factors files that specify the weights of the various travel components (e.g., transit fare, wait time, in-vehicle time, boarding and transfer penalties) are created.

Transit travel times are computed for various transit modes in the second group of steps. Travel times for mixed-flow transit vehicles are typically a function of auto times stratified by mode, area type and facility type. Travel times for vehicles that operate on exclusive right-of-way (e.g., fixed-guideway and bus-only lanes) are commonly computed using equations of motion. By default, transit speeds are set equal to auto speeds and the user has to appropriately change the speeds for all the transit modes present in the model.

Access and transfer connectors are generated in the final group of steps. Two types of access connectors are generated: walk access and auto access. Since auto connectors are built to transit stations, the template checks for the existence of stations and generates auto connectors only if there are transit stations in the highway network (transit stations are indicated by highway network node variable TSTYPE set to 1). Three types of transfer connectors are generated: one for CBD sidewalks, another to connect transit platforms, and a third to connect fixed-guideway platforms with nearby bus stops. All-walk connectors are also generated in this group of steps. Step 18 of the module is the REWALK application. Please refer to REWALK documentation located at http://www.fsutmsonline.net/images/uploads/mtf-files/Rewalk-041508.zip for more details about REWALK application.

In the Tier A template, two factors files are created: WalkTransit.Fac and AutoTransit.Fac. Also, REWALK application is not necessary for Tier A model since percent walks are not calculated for Tier A areas.

Figure 9: Transit Prep Module

## Transit Paths Module

Transit paths and skims are created (by period) in this module. As mentioned in the previous section, the Transit Paths module also runs only if transit service exists in the alternative. Figure 10 shows the module for the Tier B/C template. Walk and auto access paths and skims are built in steps 1 through 8. Four different sets of paths are built for the Tier B/C model while two sets of paths are built for the Tier A model. Transit paths for different tier areas are explained in Section 2.2 of the FSUTMS Transit Model Development Guide located at http://www.fsutmsonline.net/images/uploads/mtf-files/TM_DevelopmentGuide.pdf. All-walk paths are also generated in this module. If the highway network does not contain any transit stations, or if there are no stations with any qualifying auto access connectors, the auto access paths steps are not run and zero auto access skims are created instead.

Next, the transit paths are tested through the process of path conditioning to ensure that viable transit paths are evaluated by the mode choice model. For a path to be considered viable it must have in-vehicle time on the path (usually for a specific mode or group of modes) and it must be less onerous than an all-walk path (created in Step 9). Both tests are conducted in steps 11 (for walk-access paths) and 12 (for auto-access paths). Finally, the transit station zone number of the first boarding, the parking cost and the terminal times at the station are stored in the station-to-station matrix.

Figure 10: Transit Paths Module

## Mode Choice Module

The mode choice model is executed in this module (Figure 11 shows the module). If there is no transit service in the base year, transit skims with zeros are created and the mode choice runs. Since the transit skims are all zeros, this is essentially a highway only mode choice model.

Steps 1 through 7 involve preparations for running the mode choice utility calculations. This includes calculating the auto ownership markets, and combining the percent walk data, socio-economic data, and area type data to create a single zonal data file. Next, the travel time savings of heavy occupancy vehicles (HOVs) as compared to single occupancy vehicles (SOVs) are computed.

The mode choice utility calculations are performed in step 12. The sub-modal shares of different paths are calculated by access (can walk, must drive, and no transit) and by auto ownership. In the next step, mode choice calculations are reported in a mode choice summary report and the trip tables are combined by purpose.

The mode choice model can then be calibrated by adjusting the bias constants. Please note that this loop does not run by default. It must be activated by changing the {MC_Calib} key, which is described in Table 3 in the next chapter. The trip tables are then combined to create a single transit trip table.

For the Tier A template, percent walks are not used in the zonal data file created during mode choice preparation. Also, the sub-modal shares of different paths are calculated by auto ownership only.

Figure 11: Mode Choice Module

## Transit Assignment Module

Figure 12 below shows the Transit Assignment module. The transit assignment module runs only if there is transit service present. The auto access trips are assigned only if there are transit stations in the highway network and there are auto access connectors. The transit trip table obtained from the Mode Choice module is loaded onto the various transit paths in this module. Transit trips are assigned to paths in two different iterations by varying transit assignment parameters: legs, and links assignment. For each iteration, transit trips are assigned by period (peak and off-peak), access mode (walk and auto), and transit mode (bus and project). The auto access trips are then added to the highway trip table to be used for highway assignment.

Figure 12: Transit Assignment Module

## Transit Reporting Module

Figure 13 shows the Transit Reporting module. The reporting module runs only if there is transit service in the alternative being run. Three transit assignment reports and a network for visualization are produced in this module. TAReport module produces a summary report, a route-level report and a station activity report. Please refer to TAReport documentation located at http://www.fsutmsonline.net/images/uploads/mtf-files/TAReport-041508.zip for more details. Next, total transit volumes along corridors (by each link in the corridor) are visually displayed in a specially-prepared network.

Figure 13: Transit Reporting Module

# CHAPTER 3: Catalog keys, input and output files

This chapter details the catalog keys, input files and output files of the template. The following sections also explain the default input values and how they may be modified by the user to customize the template to fit the model at hand.

## Catalog Keys

Table 3 summarizes the catalog keys that need to be defined before running the transit model template, along with their default values (if applicable) and a brief description.

Table 3: Catalog Keys

| Catalog Key | Format | Default value | Description |
| --- | --- | --- | --- |
| {alt} | A1 | - | Alternative letter |
| {year} | A2 | - | Model year |
| {ZONESI} | I | - | Maximum internal zone number |
| {ZONESA} | A | - | Total number of zones including internal and external |
| {NODEMIN} | A | - | Minimum non-centroid node number |
| {CBDZONE} | I | - | Zone that best represents the core of the area’s Central Business District |
| {FromNode} | A | - | Origin zone number for transit path tracing |
| {ToNode} | A | - | Destination zone number for transit path tracing |
| {Units} | - | 5280 | Coordinate units per mile |
| {isMicroCode} | Boolean | - | 1 if fixed-guideway station nodes (for example skyway or BRT) are coded separately from the bus stop nodes in the network, 0 otherwise |
| {XFERACC} | - | 0.6 | Maximum cost on a transfer connector |
| {MAXWLKACCLNKS} | - | 99 | Maximum number of walk access connectors per mode |
| {WALKACC} | - | 0.6 | Maximum cost on a walk access connector |
| {AVGWLKSPD} | - | 2.5 | Average walk speed in mph (usually 2.5) |
| {AVGWALK} | - | 0.5 | Average walk distance in miles (usually 0.5 miles) |
| {MINIPCW} | - | 15 | Minimum threshold percent walk (usually 15%) |
| {OCTA} | - | 1.2 | Average auto occupancy for auto-access transit trips |
| {IsProjectMode} | Boolean | 0 | Boolean key set to 1 if the model contains a project mode, 0 otherwise (only in Tier B/C model) |
| {TERM10} | I | 5 | Terminal time (in minutes) in CBD zones |
| {TERM20} | I | 3 | Terminal time (in minutes) in CBD fringe zones |
| {TERM30} | I | 1 | Terminal time (in minutes) in residential zones |
| {TERM40} | I | 2 | Terminal time (in minutes) in OBD zones |
| {TERM50} | I | 1 | Terminal time (in minutes) in rural zones |
| {DebugMC} | - | 0 | Debug Mode Choice (greater than 0 if yes) |
| {SelOrigin} | A | - | Selected origin zone for reporting purposes |
| {SelDest} | A | - | Selected destination zone for reporting purposes |
| {hwyopcost} | F | 9.5 | Auto operating cost (cents/mile) |
| {CTOLL} | F | 0.1 | Coefficient of Toll used in assignment and pathing |
| {Zapzero} | I | 1 | Zero out the drive alone and pnr-access trips for zero-car households |
| {hbw3p} | F | 3.37 | Home-based work (HBW)- Avg 3+ Persons/Car |
| {hbo3p} | F | 3.48 | Home-based other(HBO)- Avg 3+ Persons/Car |
| {nhb3p} | F | 3.59 | Non-home based (NHB) Avg 3+ Persons/Car |
| {InflationToll} | F | 1 | Inflation factor for auto tolls |
| {InflationAOC} | F | 1 | Inflation factor for auto operating cost |
| {InflationParkCost} | F | 1 | Inflation factor for parking cost |
| {InflationFare} | F | 1 | Inflation factor for transit fare |
| {OCCPNRAccess} | F | 1.2 | Average occupancy rate for PNR access trips |
| {MinDistWalkAcc} | F | 0.6 | Minimum distance on I-J pair required for evaluation of walk-access transit paths |
| {MinDistAutoAcc} | F | 1.2 | Minimum distance on I-J pair required for evaluation of auto-access transit paths |
| {OCCKNRAccess} | F | 1.2 | Auto occupancy for KNR trips |
| {MC_Calib} | I | 0 | Mode Choice Calibration (1 if yes) |
| {RunUB} | Boolean | 0 | Dummy variable to run (=1) or not run (=0) user benefits & generate user benefit files |
| {HOVMIN} | F | 3 | Minimum time savings (in minutes) on HOV lanes before being accounted for in the mode choice equation |
| {BaseYearTransit} | I | 1 | Set to 1 if the model contains transit in base year ; 0 otherwise |

## Input files

This section describes the input file formats, required fields, naming conventions and their locations. The default versions of all the input files are already present in the model and the user has to replace them with the corresponding files for the model at hand.

### Highway networks

The highway networks that are an input to the transit model template are created by the highway model. The TMT requires two network files, an unloaded highway network file (UNLOADED_{Alt}{Year}.NET) and a pre-assigned highway network file (PREASSGN_{Alt} {Year}.NET) to be present in the output folder of the alternative. The unloaded highway network file is the basic highway network file with free flow highway speeds and capacities. The pre-assigned highway network file contains the pre-assignment speeds and volumes along with the unloaded highway network file fields. If the highway module of the model does not model congested flow (and so will not have the pre-assigned highway network), a copy of the unloaded network can be renamed PREASSGN_{Alt} {Year}.NET and used as the pre-assignment network. The following tables show the node and link variables that need to be present in the highway network files. There may be other variables present in the network files but the following variables are required to be present.

Table 4: Highway Network Link Variables

| Link variable | Type | Description | Units |
| --- | --- | --- | --- |
| A | Numeric | A node | - |
| B | Numeric | B node | - |
| DISTANCE | Numeric | Calculated distance | Miles |
| FTYPE | Numeric | Facility type | - |
| ATYPE | Numeric | Area type | - |
| TIME (unloaded highway network only) | Numeric | Free flow travel time | Minutes |
| TIME_1 (loaded highway network only) | Numeric | Congested travel time | Minutes |
| TBSTIME | Numeric | Travel time for bus transit | Minutes |
| TBSDIST | Numeric | Distance for bus transit |  |
| TBSSPEED | Numeric | Speed for bus transit | Mph |
| TFGDIST | Numeric | Distance for fixed-guideway transit | Miles |
| TFGTIME | Numeric | Travel time for fixed-guideway transit | Minutes |
| TFGMODE | Numeric | Applicable fixed-guideway transit mode | - |
| TFGSPEED | Numeric | Speed for fixed-guideway transit | Mph |

Table 5: Highway Network Node Variables

| Node variable | Type | Description | Units |
| --- | --- | --- | --- |
| N | Numeric | Node number | - |
| TSRANGE | Numeric | Maximum roadway distance allowed for auto-access connector | Miles |
| TSPARK | Numeric | Number of parking spaces (park-and-ride stations only) | - |
| TSCOSTAM | Numeric | Peak parking cost | - |
| TSCOSTMD | Numeric | Off-peak parking cost | - |
| TSPNRTERM | Numeric | Park and ride terminal time | Minutes |
| TSKNRTERM | Numeric | Kiss and ride terminal time | Minutes |
| TSTYPE | Numeric | Set to : “0” for a station not used in the alternative, “1” for a PNR/KNR station (assumed to be both), “2” for fringe park-ride locations “3” for park-ride only locations available throughout the day, “4” for kiss-ride locations, and “5” park-ride only locations available only in the peak period | - |
| TSNAME | Character | Travel time for fixed-guideway transit | Minutes |
| MPO | Numeric | A dummy number assigned to each MPO for distinction |  |
| County | Numeric | A dummy number assigned to each County for distinction |  |

### Highway skim files

The free-flow (FF) and congested-flow (CF) highway skim files are input to the AUTOCON program and the mode choice model. However, the order of tables in the skim files that AUTOCON and mode choice expect are different. Two different versions of the skim files must be made for the two programs. The skim files for both the programs must be placed in the output folder of the alternative. The following tables show the orders of tables for both the programs. The default file names for FF and CF skims used for AUTOCON are FHSKIMS_{Alt}{Year}.MAT and RHSKIMS_{Alt}{Year}.MAT (these filenames can be changed using the script that creates the transit.mas file) and those used for the mode choice module are CONGSKIM_{ALT}{YEAR}.MAT and FREESKIM_{ALT}{YEAR}.MAT respectively. As mentioned in the previous section, if the highway module of the model does not model congested flow (and so will not have the congested-flow skim), a copy of the freeflow skim can be renamed and used as the congested-flow skim.

Table 6: Highway skim tables for AUTOCON program

| Table | Name | Description |
| --- | --- | --- |
| 1 | Cost | Toll cost (in dollars) |
| 2 | Distance | Highway distance between interchange (in miles) |
| 3 | Time | Travel time (in minutes) |
| 4 | Time2 | Weighted travel time (including toll) in minutes |

Table 7: Highway skim tables for mode choice module

| Table | Name | SOV/HOV | Description |
| --- | --- | --- | --- |
| 1 | Time | SOV | Travel time (in minutes) |
| 2 | Distance |  | Highway distance between interchange (in miles) |
| 3 | Terminal Time |  | Terminal time at parking lot (in minutes) |
| 4 | Toll |  | Toll cost (in dollars) |
| 5 | Time2 |  | Weighted travel time including toll (in minutes) |
| 6 | Time | HOV | Travel time (in minutes) |
| 7 | Distance |  | Highway distance between interchange (in miles) |
| 8 | Toll |  | Toll cost (in dollars) |
| 9 | Time2 |  | Weighted travel time including toll (in minutes) |

### Production trip rate file (GRATES)

This file is used in the mode choice module to determine the zero, 1, and 2+ car percentages for each zone. It is a DBF file (in the output folder of the model) with the following default field names.

Table 8: Columns in the GRATES File

| Column | Name | Description |
| --- | --- | --- |
| 1 | COUNTER | Row number for lookup (1 through 45) |
| 2 | PPDU | Number of persons in the household |
| 3 | APDU | Number of autos in the household |
| 4 | DUTYPE | Dwelling unit type |
| 5 | HBWPR | HBW production rate |
| 6 | HBSHPR | HBShopping production rate |
| 7 | HBSRPR | HBSocialRec production rate |
| 8 | HBOPR | HBO production rate |

### Dwelling unit weights file (DUWEIGHTS)

This file is also used in the mode choice module. It is a DBF file (in the output folder of the model) with the following default field names.

Table 9: Columns in the DUWEIGHTS File

| Column | Name | Description |
| --- | --- | --- |
| 1 | SIZERANGE | Row number (1 through 17) representing size ranges |
| 2 | PCT1PER | Percent of 1 person units |
| 3 | PCT2PER | Percent of 2 person units |
| 4 | PCT3PER | Percent of 3 person units |
| 5 | PCT4PER | Percent of 4 person units |
| 6 | PCT5PER | Percent of 5+ person units |

### Person trip file (PSNTRIPS_{Alt}{Year}.MAT)

The mode choice model expects the “HBW”, “HBO” and “NHB” purpose trip tables (with those table names and order) from the person trip file. This file must be placed in the output folder of the alternative. The module also expects fourth and fifth tables in the person trip file to be “TRKTAXI” and “IE” vehicle trips. Step 26 in the mode choice module combines these two trip table with the output person trips from the mode choice model run to create a vehicle trip table for the final highway assignment.

### Zonal data files

The zonal data files (placed in input folder of the alternative) contain information about the zones in the model. The user can have more than one data file, and may also have field names other than the ones used by default. Section 4.10 mentions the changes in scripts in order to use alternate variable names. Table 10 shows the default fields used in the model.

Table 10: Required fields in zonal data files

| Field | Description |
| --- | --- |
| TAZ | Zone number |
| SFDU | Total single family dwelling units |
| SF_PCTVNP | Percent households seasonal+vacant |
| SF_PCTVAC | Percent households vacant |
| SFPOP | Population in single families |
| SF_0AUTO | Percent zero car households in single families |
| SF_1AUTO | Percent one car households in single families |
| SF_2AUTO | Percent two car households in single families |
| MFDU | Total multiple family dwelling units |
| MF_PCTVNP | Percent households seasonal+vacant |
| MF_PCTVAC | Percent households vacant |
| MFPOP | Population in multiple families |
| MF_0AUTO | Percent zero car households in single families |
| MF_1AUTO | Percent zero car households in single families |
| MF_2AUTO | Percent zero car households in single families |
| HMDU | Number of hotel/motel rooms |
| HMOCC | Percent hotels/motels occupied |
| HMPOP | Population in hotels/motels |
| SHORTPARK | Short term parking cost |
| LONGPARK | Long term parking cost |

### Transit line file (TROUTE_{year}{alt}.LIN)

The transit line file must represent all time periods in order to simplify data maintenance. Each line is coded with at least two headways (PT can accommodate up to five), one for the AM peak period and another for the off-peak period. If a line does not conduct service in any time period, the headway should be coded as zero for that time period. Two-way coding is used for those lines whose routing does not vary in either direction. The transit line fields and their recommended values are shown in Table 11. The default transit line file has two transit lines and may be used as a guide to code the transit lines of the model. The user has to code the transit lines corresponding to his/her model in the transit line file. The transit line file can be coded manually offline and must be stored in the input folder of the alternative. The keyword N can have sub-keywords to add further details within the node list to show dwell times and layovers. This is explained in Table 12.

Table 11: Keywords to LINE Control Statement and Their Recommended Values

| Keyword to LINE control statement | Type | Description | Recommended Value |
| --- | --- | --- | --- |
| LONGNAME | Character | 40-character description | None |
| NAME | Character | 10-character description | None |
| ONEWAY | Boolean | If true line travels in coded direction. If false, line travels in both directions | None |
| HEADWAY[1] | Numeric | Time between consecutive vehicles (1=peak period; 2=offpeak period) | Minutes (0 if not offered in period) |
| HEADWAY[2] | Numeric |  |  |
| MODE | Numeric | Transit mode (defined in system data file) | None |
| OPERATOR | Numeric | Transit operator (defined in system data file) | None |
| N | Numeric string | String of nodes traversed | Positive if vehicle stops for boarding, negative if vehicle does not stop |
| TIME | Numeric | Sets the actual node-to-node travel time | None |
| CIRCULAR | Boolean | If true, the line is circular (it operates in a loop or circle). If false, the line is not circular | None |

Table 12: Sub-keywords to Keyword N in LINE Control Statement

| Sub-keywords to N | Example | Description |
| --- | --- | --- |
| DELAY | N=5001,5002,DELAY=5,5004 | Additional time delay (minutes) added to link time |
| DWELL | N=5001,5002,DWELL=8,5004 | Dwell time (minutes) at preceding node |

### System file (TSYSD.pts)

The system data file defines the modes, transit operators, vehicle types and wait-curves used in the transit system. This file is stored in the parameters folder of the model. The default system file present in the template is for guidance only. The user needs to change this file to tailor it to his/her model. The modes and operators used in the default file are explained below.

- Mode definitions

The default mode definitions used in the transit model template are summarized in the table below. The first 20 mode numbers are reserved for non-transit modes. Each transit route in the transit line file is assigned a mode number. To assist in New/Small Starts analysis, mode 26 is reserved for “other mode” (i.e., a new transit mode that is built between the base and horizon years) and mode 27 is reserved for “project mode” (i.e., the mode under analysis), respectively. The user can define additional modes in the TSYSD.PTS file.

Table 13: Default Modes and Mode Numbers in SYSTEM.PTS File

| Mode | Number | Type |
| --- | --- | --- |
| Walk connectors | 1 | Non-transit mode |
| PNR connectors | 2 | Non-transit mode |
| All walk connectors | 4 | Non-transit mode |
| Transfer connectors | 11 | Non-transit mode |
| Sidewalk connectors | 12 | Non-transit mode |
| Local bus | 21 | Transit mode |
| Premium service | 22 | Transit mode |
| Circulators (trolley/streetcar) | 23 | Transit mode |
| Urban(light/heavy) rail | 24 | Transit mode |
| Commuter rail | 25 | Transit mode |
| Other mode | 26 | Transit mode |
| Project mode | 27 | Transit mode |

- Operator definitions

Operators represent different types of services offered by a system. Operators are also used to define the boarding and transfer fares. Each line is assigned an operator number and the fare attached to the line is mapped to the operators in the factors file. The default operators defined in the transit model template are shown in the table below.

Table 14: Default Operators, Operator Numbers, and FareSystems in TSYSD.PTS File

| Operator | Operator number | FareSystem |
| --- | --- | --- |
| Local service | 1 | 1 |
| Circulator | 2 | 2 |
| Commuter rail | 3 | 3 |

### Fares file (TFAREStp_{year}{alt}.FAR)

Fare structures are defined in the fares file and stored in the input folder of the alternative. A fare structure is related to each transit route using its operator number in the factors file. It is not important that the fare system number correspond to the operator number. Three fare systems are likely to be used: free, flat, and zone-based. The first system is for services that are offered for free. Flat-fare systems charge flat boarding and transfer fares regardless of journey length. Zone-based fare systems base the fare on the number of fare zones encountered during a trip. When using zone-based systems, it is important to remember to code FAREZONE on the node of each station in the highway network. The recommend values for all fare systems are shown below.

Table 15: Keywords to FARESYSTEM Control Statement and Their Recommended Values

| Keyword to FARESYSTEM control statement | Description | Recommended value |
| --- | --- | --- |
| NUMBER | Fare system number | None |
| LONGNAME | 40-character description | None |
| NAME | 10-character description | None |
| STRUCTURE | Type of fare system | “FREE” (free) “FLAT” (flat-fare) “ACCUMULATE” (zone-based) |
| SAME | Determines how the fare is produced for consecutive legs using the same fare system | n/a (free) “CUMULATIVE” (flat-fare & zone-based) |
| IBOARDFARE | Initial boarding fare (in dollars) | n/a (free) None (flat-fare & zone-based) |
| FAREFROMFS | Transfer fares when transferring from other fare systems | n/a (free) None (flat-fare & zone-based) |

The default fares file present in module are for guidance and need to be changed by the user to reflect the fares of the model at hand. The boarding and transfer fares used in the default file are shown below.

Table 16: Default Fares Used In the Fares File

| Operator | Boarding Fare | FareSystem |
| --- | --- | --- |
| Local service | $1.50 | 1 |
| Circulator | $0.00 | 2 |
| Commuter Rail | $2.00 | 3 |

Table 17: Default Transfer Fares Used In the Fares File

| Faresystem | From To | 1 | 2 | 3 |
| --- | --- | --- | --- | --- |
| 1 | Free | 1.50 | Free |
| 2 | Free | Free | Free |
| 3 | 0.50 | 2.00 | Free |

### Transit Coefficients file (TRN_COEFFICIENTS.DBF)

This file is named TRN_COEFFICIENTS.DBF and is located in the parameters folder. The CBD constants are also in this file. Their default values are set to 1.00 for Tier B/C and 0.00 for Tier A template and need to be calibrated by the user.

Table 18: Default Transit Coefficients for Tier B/C

### Mode Choice constants file (MC_CONSTANTS.DBF )

This file contains the utility and nesting constants, and is located in parameters folder. The default constants are all set to -1.00 and need to be adjusted by the user. Utility constants having a value of -999.99 effectively mandate zero trips for that particular utility. The table below shows the default constants used in the template for Tier B/C. The choices that do not exist in Tier A cities will have values of -999.99.

Table 19: Default Mode Choice Constants for Tier B/C

### Percent walk file (PCWALK_{Year}{Alt}.DAT)

The percent walk of a zone is the proportion of the zonal area within walking distance to transit. This file is generated offline using a GIS buffer of 0.5 mile around the stops. Individual percent walk values are generated for peak and off-peak transit services. The percent walk at attraction end of the trip is twice the percent walk at the production end to reflect that attractions are normally oriented near major streets where transit is located. The format of the percent walk file is shown in the Table 20. The percent walks need to be generated by the user for every alternative. Percent walks are generated for the Tier B/C model only.

Table 20: Percent Walk File Format

| Columns | Format | Description |
| --- | --- | --- |
| 1-5 | I4 | TAZ |
| 6-11 | I3 | Peak period percent walk at production-end of the trip |
| 12-17 | I3 | Peak period percent walk at attraction-end of the trip |
| 18-23 | I3 | Off-peak period percent walk at production-end of the trip |
| 24-29 | I3 | Off-Peak period percent walk at attraction-end of the trip |

### Mode choice targets (MC_TARGETS.DBF)

This file contains the mode share targets obtained from on-board surveys. When the mode choice model is calibrated, the model shares are matched with the shares present in this file. This file is located in parameters folder. The default shares for Tier B/C template are shown in Table 22 below and need to be changed by the user to reflect the shares calculated from surveys.

Table 21: Default Mode Share Targets for Tier B/C

| No. | HBW | HBO | NHB | Market | Description |
| --- | --- | --- | --- | --- | --- |
| 1 | 0.0000 | 0.0000 | 0.4770 | Zero car households | Drive alone |
| 2 | 0.6610 | 0.5700 | 0.3000 |  | Shared ride 2 |
| 3 | 0.2310 | 0.3960 | 0.2170 |  | Shared ride 3+ |
| 4 | 0.1040 | 0.0330 | 0.0040 |  | Walk to bus |
| 5 | 0.0000 | 0.0000 | 0.0000 |  | Walk to project |
| 6 | 0.0000 | 0.0000 | 0.0010 |  | PNR bus |
| 7 | 0.0000 | 0.0000 | 0.0000 |  | PNR project |
| 8 | 0.0040 | 0.0010 | 0.0010 |  | KNR bus |
| 9 | 0.0000 | 0.0000 | 0.0000 |  | KNR project |
| 10 |  |  |  | Not used |
| 11 |  |  |  | Not used |
| 12 |  |  |  | Not used |
| 13 | 0.7690 | 0.3760 | 0.0000 | One car households | Drive alone |
| 14 | 0.1520 | 0.3570 | 0.0000 |  | Shared ride 2 |
| 15 | 0.0600 | 0.2630 | 0.0000 |  | Shared ride 3+ |
| 16 | 0.0150 | 0.0030 | 0.0000 |  | Walk to bus |
| 17 | 0.0000 | 0.0000 | 0.0000 |  | Walk to project |
| 18 | 0.0020 | 0.0006 | 0.0000 |  | PNR bus |
| 19 | 0.0000 | 0.0000 | 0.0000 |  | PNR project |
| 20 | 0.0020 | 0.0004 | 0.0000 |  | KNR bus |
| 21 | 0.0000 | 0.0000 | 0.0000 |  | KNR project |
| 22 |  |  |  | Not used |
| 23 |  |  |  | Not used |
| 24 |  |  |  | Not used |
| 25 | 0.7800 | 0.3800 | 0.0000 | Two+ car households | Drive alone |
| 26 | 0.1540 | 0.3530 | 0.0000 |  | Shared ride 2 |
| 27 | 0.0610 | 0.2650 | 0.0000 |  | Shared ride 3+ |
| 28 | 0.0030 | 0.0010 | 0.0000 |  | Walk to bus |
| 29 | 0.0000 | 0.0000 | 0.0000 |  | Walk to project |
| 30 | 0.0010 | 0.0005 | 0.0000 |  | PNR bus |
| 31 | 0.0000 | 0.0000 | 0.0000 |  | PNR project |
| 32 | 0.0010 | 0.0005 | 0.0000 |  | KNR bus |
| 33 | 0.0000 | 0.0000 | 0.0000 |  | KNR project |
| 34 |  |  |  | Not used |
| 35 |  |  |  | Not used |
| 36 |  |  |  | Not used |
| 37 | 0.1480 | 0.1700 | 0.1070 | CBD walk constant |
| 38 | 0.8400 | 0.5000 | 0.5000 | CBD PNR constant |
| 39 | 0.3130 | 0.3330 | 0.1140 | CBD KNR constant |

## Key output files

### Highway Vehicle Trip Table (HWYTTAB_{Alt}{Year}.MAT)

The HBW, HBO and NHB person trips are converted to vehicle trips in the mode choice module and are assembled together with the truck/taxi and IE trips to create a vehicle trip table for the final highway assignment. By default, the IE trips are divided equally between “SOVIETrips” and “HOVIETrips” in the transit model template.

Table 22: Tables in the vehicle trip tables

| Table | Name | Description |
| --- | --- | --- |
| 1 | DriveAlone | Drive alone trips |
| 2 | Carpool | Shared ride trips |
| 3 | TruckTaxi | Truck and taxi trips |
| 4 | EETrips | External-external trips |
| 5 | SOVIETrips | SOV Internal-External trips |
| 6 | HOVIETrips | HOV Internal-External trips |

### Person Trip Table (MODEOUT.MAT)

Tier A transit model template outputs a person trip table file with 18 tables – 6 choices (Drive alone, shared ride 2, shared ride 3+, Walk to Transit, PNR Access to Transit and KNR Access to Transit) for each of the three purposes. For Tier B/C, this file contains 27 tables – 9 choices for each of the three purposes.

### Transit assignment summary report (TASUM_{ALT}{YEAR}.PRN)

This report is located in the output folder and presents the travel time, frequency, number of passengers, passenger miles, passenger hours, and maximum load by route, mode, and operator. The following table shows the formatting used in this file and the figure below shows a screenshot.

Table 23: Transit Assignment Summary Report Format

| Period | Field | Columns | Format | Description |
| --- | --- | --- | --- | --- |
| Route | Route Name | 1-16 | Character | 10-character description |
|  | Mode | 21-25 | Numeric | Mode number |
|  | Optr | 26-30 | Numeric | Operator number |
|  | Dist | 31-40 | Numeric | Distance in miles |
|  | Route Longname | 202-241 | Character | 40-character description |
| Peak | Time | 41-50 | Numeric | Transit travel time in minutes |
|  | Freq | 51-60 | Numeric | Transit service frequency in minutes |
|  | Pax | 61-70 | Numeric | Total number of passengers boarding a transit route |
|  | Maxld | 71-80 | Numeric | Maximum passenger load of a transit route |
|  | PaxMi | 81-90 | Numeric | The total passenger miles of a transit route |
|  | PaxHr | 91-100 | Numeric | The total passenger hours of a transit route |
| Off-Peak | Time | 101-110 | Numeric | Transit travel time in minutes |
|  | Freq | 111-120 | Numeric | Transit service frequency in minutes |
|  | Pax | 121-130 | Numeric | Total number of passengers boarding a transit route |
|  | Maxld | 131-140 | Numeric | Maximum passenger load of a transit route |
|  | PaxMi | 141-150 | Numeric | The total passenger miles of a transit route |
|  | PaxHr | 151-160 | Numeric | The total passenger hours of a transit route |
| Daily | Pax | 161-170 | Numeric | Total number of passengers boarding a transit route |
|  | Maxld | 171-180 | Numeric | Maximum passenger load of a transit route |
|  | PaxMi | 181-190 | Numeric | The total passenger miles of a transit route |
|  | PaxHr | 191-200 | Numeric | The total passenger hours of a transit route |

Figure 14: Transit Assignment Summary Report (Snippet)

### Transit Assignment Route-Level Report (TASROUTE_{ALT}{YEAR}.PRN)

This report is located in the output folder and presents the leg travel time, the cumulative travel time, ons, offs, leg distance, cumulative distance and the load for all the routes. The following table shows the formatting used in this file and the figure below shows a screenshot.

Table 24: Transit Assignment Route-Level Report Format

| Period | Field | Columns | Format | Description |
| --- | --- | --- | --- | --- |
| Link | Node | 3-7 | Numeric | Anode in anode→bnode link of a transit route |
|  | Dist | 8-17 | Numeric | Distance of anode→bnode link in miles |
|  | CumDist | 18-27 | Numeric | Cumulative distance of a transit route till that link |
| Peak | Time | 28-37 | Numeric | Transit travel time of anode→bnode link in minutes |
|  | CumTime | 38-47 | Numeric | Cumulative travel time of a transit route till that link |
|  | On | 48-57 | Numeric | Boardings at anode in anode→bnode direction |
|  | Off | 58-67 | Numeric | Alightings at anode in anode→bnode direction |
|  | Load | 68-77 | Numeric | Passenger load carried from anode to bnode |
| Off-Peak | Time | 78-87 | Numeric | Transit travel time of anode→bnode link in minutes |
|  | CumTime | 88-97 | Numeric | Cumulative travel time of a transit route till that link |
|  | On | 98-107 | Numeric | Boardings at anode in anode→bnode direction |
|  | Off | 108-117 | Numeric | Alightings at anode in anode→bnode direction |
|  | Load | 118-127 | Numeric | Passenger load carried from anode to bnode |
| Daily | On | 128-137 | Numeric | Boardings at anode in anode→bnode direction |
|  | Off | 138-147 | Numeric | Alightings at anode in anode→bnode direction |
|  | Load | 148-157 | Numeric | Passenger load carried from anode to bnode |

Figure 15: Transit Assignment Route- Level Report (Snippet)

### Station Activity Report (Stations_{Alt}{Year}.prn)

The station activity report, located in the output folder, presents the frequency of all the transit services visiting the station, the number of passengers accessing and egressing the station, and the boardings and alightings at the station.

The access and egress data presented in this report are based on P-to-A assignment. For example, if there are 100 trips from zone i to zone j, and 60 trips from zone j to zone i, P-to-A assignment assigns 160 trips in the i-j direction. The user will have to post process this information to produce O-D results. It should be noted that the boardings at a station can exceed the sum of accesses from all access modes as there can be transfers between transit routes at a station. Such transfers appear in the boardings but not in any of the access modes.

Figure 16: Station Activity Report (Snippet)

    - TMT Runtime Report (TMTtime.prn)

The transit model template runtime report, located in the output folder, stores the time and date stamp for the completion of each of the six modules of the TMT. The report also notes the existence/lack of existence of the TMT input files and the input and output files for AUTOCON program. This can be very handy when there is a model run crash and the user wants to debug the run. By referring to the report, the user can know the last module that was successfully run and can identify the time periods for each module run to get an idea if the module was run completely. If the model crashes due to a missing input file, this will also be noted in the runtime report. The figure below shows a screenshot of the report.

# CHAPTER 4: Changes in scripts

This chapter details the parts of scripts that the user may adjust in order to customize the template for individual models. The adjustments discussed in this chapter represent the minimum amount needed but there may be other scripts or other parts in the discussed scripts that the user may have to adjust in the model. The step numbers mentioned in this chapter corresponds to the step numbers in the Tier B/C transit model template. The script sections that the user has to adjust are denoted in the scripts by the following opening and closing lines:

;**************************************************************

; BEGIN POTENTIAL SCRIPT ADJUSTMENT

;**************************************************************

;**************************************************************

; END POTENTIAL SCRIPT ADJUSTMENT

;**************************************************************

## Compatibility Module Scripts

The compatibility module scripts (CPMAT00A.S, CPMAT00B.S, CPMAT00C.S, CPMAT00D.S, and CPNET00A.S) are located in the Compatibility module. These scripts must be used to make the highway model output files compatible with the transit model template formats. These script files are empty and the user has to write the script ONLY when any of the input files are not in the format that the TMT expects (see Section 3.2 for the TMT input file formats). The execution orders of these steps are set to zero and if the user has to run these steps in the model, the execution order must be changed to a number greater than zero.

## TPNET00C.S  (Transit speed for peak period)

This script file is located in the Transit Prep module (second module in the transit model template). In this module, open the script file for NETWORK step 8 (Transit speed for peak period). The peak period speeds for the various transit modes (modes 21 through 27 in the default case) are defined in this script.

By default, all the transit mode speeds are set equal to auto speeds. The user has to apply appropriate logic in this section to define the transit speeds to be used in the model. In the default case, the variable for the speed of transit mode 21 is _TSPD21. Similarly, the variables for the speeds of transit modes 22 through 27 are _TSPD22 through _TSPD27. The user may follow the same naming convention to define transit speeds for new transit modes being defined. After defining the new transit speeds, the user has to delete the lines that set the default peak transit speeds for transit modes. At the end of this step, the variables _TSPD21, _TSPD22, _TSPD23, _TSPD24, _TSPD25, _TSPD26, _TSPD27, and the similar variables for any new transit modes must contain the speed for that transit mode.

## TPNET00C.S (Transit speed for offpeak period)

This script file is located the Transit Prep module. In this module, open the script file for NETWORK step 9 (Transit speed for offpeak period). The offpeak period speeds for the transit modes are defined in this script. The user has to delete those lines from the script file that set the default offpeak transit speeds for transit modes, just as in Section 4.1 and define new transit mode speeds.

## TPPTR00A.S (Build peak access connectors)

This script file is located in “Transit Prep” module. In this module, open the script file for PUBLIC TRANSPORT step 12 (Build peak access connectors). In this script, TRANTIME[xx] denotes the transit time for mode number xx. If the user defines transit times for new transit modes in a model, the transit times of these modes can be added in this script file. If the transit time of a mode is not added here, it is assigned the transit time of mode 21 (local bus) by default. A comma needs to be added at the end of each transit time definition except the last.

## TPPTR00B.S (Build offpeak access connectors)

This script file is located in “Transit Prep” step (step 1). In this step, open the script file for PUBLIC TRANSPORT step 14 (Build offpeak access connectors). The transit times for new user defined modes can be added here similar to the TPPTR00A.S script in Section 4.3 above.

## TRPTR00A.S (Walk-Access Paths/Skims – peak)

This script file is located in the Transit Paths module (third module in the transit model template). In this step, open the script file for PUBLIC TRANSPORT step 2 (Walk-Access Paths/Skims – peak). Two separate sections are identified for adjustment in the script. In the first section, the transit times for new user defined modes can be similar to the TPPTR00A.S script in Section 4.3 above. In the second section, the travel times are calculated for all the modes of the model and this is used to develop the transit skims. If the user defines new modes in a model, accordingly, they need to be added in the skim files. For example, if the user defines a new local bus service mode with mode number 31, and a new commuter rail mode 34, then this section must be changed to read the following:

PROCESS PHASE=SKIMIJ

MW[1]=TIMEA(0,1)                                                        ; Walk time

MW[2]=TIMEA(0,2)                                                        ; Auto time

MW[3]=TIMEA(0,11)+TIMEA(0,12)                                           ; Sidewalk time

MW[4]=TIMEA(0,21)+TIMEA(0,31)                                           ; Local bus time

MW[5]=TIMEA(0,22)                                                       ; Premium bus time

MW[6]=TIMEA(0,23)                                                       ; Circulator time

MW[7]=TIMEA(0,24)+TIMEA(0,34)                                           ; Light/Heavy Rail time

MW[8]=TIMEA(0,25)                                                       ; Commuter Rail time

MW[9]=TIMEA(0,26)                                                       ; Other mode time

MW[10]=TIMEA(0,27)                                                      ; Project mode time

## TRPTR00B.S (Auto-Access Paths/Skims – peak)

This script file is located in the Transit Paths module. In this step, open the script file for PUBLIC TRANSPORT step 4 (Auto-Access Paths/Skims – peak). The changes that need to be made in this script file are similar to the changes to be made in TRPTR00A.S in Section 4.5 above.

## TRPTR00C.S (Walk-Access Paths/Skims – offpeak)

This script file is located in the Transit Paths module. In this step, open the script file for PUBLIC TRANSPORT step 6 (Walk-Access Paths/Skims – offpeak). The changes that need to be made in this script file are similar to the changes to be made in TRPTR00A.S in Section 4.5 above.

## TRPTR00D.S (Auto-Access Paths/Skims – offpeak)

This script file is located in the Transit Paths module. In this step, open the script file for PUBLIC TRANSPORT step 8 (Auto-Access Paths/Skims – offpeak). The changes that need to be made in this script file are similar to the changes to be made in TRPTR00A.S in Section 4.5 above.

## MCPREP.S (Auto ownership percentage by TAZ for work and non-work purposes)

This script file is located in the Mode Choice Model module. In this step, open the script file for MATRIX step 5 (Auto ownership %age by TAZ for work and non-work purposes). This script computes the work and non-work purpose auto ownership percentages at a TAZ. If the model consists of a number of regions with different sets of trip generation rates, each of them can be accommodated in this step. By default, only one set of trip generation rates are used in the script. The user can modify this script to add more sets of trip generation rates. In order to do so, the user has to add a file that maps the TAZs to different sets of rates, and the files that contain the different sets of trip generation rates.

The script file provides an example of this with some commented lines. It must be noted that by default, only one set of trip generation rates is used (GRATES_MC.DBF). The script contains some commented lines that demonstrate a case of multiple sets of trip generation rates. This is intended for guidance only. The user needs to change this file appropriately to tailor it to his/her model. In the example, the model has three MPOs and each MPO has a different set of trip generation rates. The mapping file contains the MPO number of each TAZ. A section of the script file reads the following:

;LOOKUP LOOKUPI=3,

;       NAME=TYPE,

;         LOOKUP[4]=1, RESULT=5,         ; Two-digit area type

;         LOOKUP[5]=1, RESULT=6,         ; County

;         LOOKUP[6]=1, RESULT=7,         ; MPO

;       FAIL[1]=0,FAIL[2]=0,FAIL[3]=0

In these lines, the lookup file that maps TAZ numbers with MPO numbers is read in. The first column of the lookup file is the TAZ number. Column 5 contains the two-digit area type, column 6 contains the county number and column 7 contains the MPO number. Now, different sets of generation rates can be based on area type or county or MPO. MPO numbers are used in this example. The user has to similarly add and read in a lookup file that maps the TAZs to different sets of trip generation rates.

The following lines of the script read in the trip generation rates from the two MPOs (other than the default MPO):

;LOOKUP LOOKUPI=4,

;       NAME=RATES2,

;         LOOKUP[1]=COUNTER, RESULT=PPDU,

;         LOOKUP[2]=COUNTER, RESULT=APDU,

;         LOOKUP[3]=COUNTER, RESULT=DUTYPE,

;         LOOKUP[4]=COUNTER, RESULT=HBWPR,

;         LOOKUP[5]=COUNTER, RESULT=HBSHPR,

;         LOOKUP[6]=COUNTER, RESULT=HBSRPR,

;         LOOKUP[7]=COUNTER, RESULT=HBOPR,

;       FAIL[1]=0,FAIL[2]=0,FAIL[3]=0

;LOOKUP LOOKUPI=5,

;       NAME=RATES3,

;         LOOKUP[1]=COUNTER, RESULT=PPDU,

;         LOOKUP[2]=COUNTER, RESULT=APDU,

;         LOOKUP[3]=COUNTER, RESULT=DUTYPE,

;         LOOKUP[4]=COUNTER, RESULT=HBWPR,

;         LOOKUP[5]=COUNTER, RESULT=HBSHPR,

;         LOOKUP[6]=COUNTER, RESULT=HBSRPR,

;         LOOKUP[7]=COUNTER, RESULT=HBOPR,

;       FAIL[1]=0,FAIL[2]=0,FAIL[3]=0

The user has to similarly add and read in lookup files that correspond to the different trip generation rates of the different model regions. So, the file that maps TAZs to MPOs and the files that contain the trip generation rates of the three MPOs are read in. The MPO number of a TAZ is identified in the following IF loop in the example case:

;_mpo = TYPE(5,I)

;_gendist = 1

;IF (_mpo==1)          ; Region 1

;  _gendist = 1

;ELSEIF (_mpo==2)      ; Region 2

;  _gendist = 2

;ELSEIF (_mpo==3)      ; Region 3

;  _gendist = 3

;ENDIF

The user has to similarly add an IF loop that notes the different model regions that contain different trip generation rates.

In the example, three different rates of trip generations are read in the following lines:

;  IF (_gendist==1)

_HMTRIP  = RATES1(L+3,_tmp1)*HMDUM[x]

_SFTRIP1 = RATES1(L+3,_tmp2)*SFDUM1[x]

_SFTRIP2 = RATES1(L+3,_tmp3)*SFDUM2[x]

_SFTRIP3 = RATES1(L+3,_tmp4)*SFDUM3[x]

_MFTRIP1 = RATES1(L+3,_tmp5)*MFDUM1[x]

_MFTRIP2 = RATES1(L+3,_tmp6)*MFDUM2[x]

_MFTRIP3 = RATES1(L+3,_tmp7)*MFDUM3[x]

;    ELSEIF (_gendist==2)

;      _HMTRIP  = RATES2(L+3,_tmp1)*HMDUM[x]

;      _SFTRIP1 = RATES2(L+3,_tmp2)*SFDUM1[x]

;      _SFTRIP2 = RATES2(L+3,_tmp3)*SFDUM2[x]

;      _SFTRIP3 = RATES2(L+3,_tmp4)*SFDUM3[x]

;      _MFTRIP1 = RATES2(L+3,_tmp5)*MFDUM1[x]

;      _MFTRIP2 = RATES2(L+3,_tmp6)*MFDUM2[x]

;      _MFTRIP3 = RATES2(L+3,_tmp7)*MFDUM3[x]

;    ELSEIF (_gendist==3)

;      _HMTRIP  = RATES3(L+3,_tmp1)*HMDUM[x]

;      _SFTRIP1 = RATES3(L+3,_tmp2)*SFDUM1[x]

;      _SFTRIP2 = RATES3(L+3,_tmp3)*SFDUM2[x]

;      _SFTRIP3 = RATES3(L+3,_tmp4)*SFDUM3[x]

;      _MFTRIP1 = RATES3(L+3,_tmp5)*MFDUM1[x]

;      _MFTRIP2 = RATES3(L+3,_tmp6)*MFDUM2[x]

;      _MFTRIP3 = RATES3(L+3,_tmp7)*MFDUM3[x]

; ENDIF

The user has to similarly add an IF loop that reads in different trip generation rates corresponding to different model regions.

## MCPREP.S and MCMAT00B.S

These two scripts are located in the Mode Choice Model module. In this step, MCPREP.S is the script file for MATRIX step 5 and MCMAT00B.S is the script file for MATRIX step 6. In these two scripts, the default zonal data file variables mentioned in Section 3.2.11 are used. The user may change these scripts to use alternative variable names. A variable X is used in the script as ZI.1.X and if the variable name is to be changed to Y, all instances of ZI.1.X in these two scripts need to be changed to ZI.1.Y.

# Appendix: Transit Model Tier A Template Screenshots

Figure 17: Transit Prep Module

Figure 18: Transit Paths Module

Figure 19: Mode Choice Module

Figure 20: Transit Assignment Module

Figure 21: Transit Reporting Module