## Slide 1: SERPM 8 NPMRDS SPEED DATA
---------
8/29/2017
Marty Milkovits, Xuemei Liu

## Slide 2: Outline
Description of data sources
Methodology
Initial Results and findings

## Slide 3: Description of validation data sources
2015 NPMRDS Data*
  April 1st to 30th 2015 weekdays & weekends
  1-hour interval average speed data from vehicle probe
2015 Here Data**
  April 1st to 30th 2015 weekdays & weekends
  Speed data with high confidence (>0.7)
24-hour Count Data
  April 1st to 30th 2015 weekdays & weekends
  2014 Stations Available
*Data downloaded from RITIS Probe Data Analytics Suite. https://vpp.ritis.org/suite/download/
Notes: * and ** are downloaded from https://vpp.ritis.org/suite/download/
**Used to cross-check NPMRDS data
Username: xliu@camsys.com
Password: lxm123456

## Slide 4: Approach
Use NPMRDS speed data to identify NHS network links with valid speed data:
Identify valid links in NHS
All +/- TMC have been removed and only N/P TMC kept
Attach TMC to NHS
The TMC identification table is processed to establish the multiple-to-multiple correspondence between TMCs and NHS links*
The multiple-to-multiple correspondence is cleaned up in consideration of the duplicated LINK_ID
Each LINK_ID is only associated with one TMC for each direction **
Notes: *Xuemei conducted these two steps in ArcGIS
**See line 53-63 of X:\Proj\2016\160136 - FLDOT D4 UMdlDev16_OnCall\Validation\data\Speeds\version_0808\Speed_0905.R

## Slide 5: Link Direction Identification
Image Source: Inrix (2014). I-95 Vehicle Probe Project II. page 81 & 82.
http://i95coalition.org/wp-content/uploads/2015/02/I-95-VPP-II-INRIX-Inteface-Guide-v1-Dec-2014.pdf?dd650d
Notes: After discussion, only data of N & P are selected.

## Slide 6: Approach
Attach TMC from NPMRDS speed data to highway network links using count station lookup, or spatial join between highway network and NHS network shape file.
Only NHS links close to highway count station (50 feet) with 24-hour counts and Highway network links close to NHS links with valid speed data(200 feet) would be considered
65% links are joined with TMC based on shared LINK_ID between Master network and NHS network
Others are joined based on the spatial relationship between NHS and latest highway network

## Slide 7: Approach
Calculate 5th and 50th percentile hourly speed using average speed data from the NPMRDS speed data for highway links with TMC attached
  5th percentile speed correlates with congested speed
  50th percentile speed is calculated to replace outliers of 5th percentile speed if any
Notes: *From Dan Beagan’s email

## Slide 8: Approach
Calculate weighted daily average speed or TOD using hourly counts data
Calculate 85th percentile average speed for each link for all time periods as reference speed, and reference speed has been rounded to the nearest 5 mph

## Slide 9: Initial Results
Tabulate speed data by facility type and area type
Compare reference speed with free-flow speed and posted speed

## Slide 10: FTC2 Tabulation

## Slide 11: Links matched
Categories | # of TMC
CBD | 83
Fringe | 55
OBD | 472
Generally Residential | 1,169
Rural | 101
Total | 1,880
FTC2 | Categories | # of TMC
11 | Freeway | 201
12 | Freeway-type II | 6
21 | Uninterrupted Segment | 58
41 | Hi-Speed (Arterials) | 1,274
61 | Low-speed Collectors | 113
71 | On Ramp | 7
72 | Loop On | 2
73 | Off Ramp | 6
74 | Loop Off | 1
75 | Freeway-to-Freeway (included in FRWY) | 5
91 | Freeway Segments | 162
92 | Uninterrupted Segments | 6
93 | On | 17
94 | Off | 2
 | Total | 1,880

## Slide 12: Average Speed by Area Type
5 percentile speed
  TOD
    AM Peak (6AM – 9AM)
    Midday (9AM – 3PM)
    PM Peak (3PM – 7PM)
    Evening (7PM – 10PM)
    Night (10PM – 6AM)
  ATG
    1  CBD
    2  Fringe
    3  OBD
    4  Generally Residential
    5  Rural
Notes: Average speed increases from CBD to Rural for roadways of all facility types

## Slide 13: Average Speed by Area Type
Chart: 5th Percentile Average Speed by Area Type
AM speed | 26.6746 | 29.4474 | 29.5795 | 33.215 | 43.4731
Midday speed | 26.1062 | 28.6854 | 29.4564 | 32.9139 | 43.0954
PM speed | 24.5357 | 24.9516 | 27.2008 | 31.7936 | 43.484
Evening speed | 26.7225 | 30.3068 | 30.6894 | 33.5505 | 43.7991
Night speed | 27.9703 | 33.6737 | 33.0969 | 35.0327 | 44.2011

## Slide 14: Average Speed by Functional Class
5 percentile speed
  FTC*
    10  Freeway
    20  Uninterrupted Facility
    40  Higher Speed Interrupted Facility
    60  Lower Speed & Collector Facility
    70  Ramps
    90 Toll Roads
Notes: As shown in the blue rectangular, AM, PM and Midday average speed are quite similar for arterials and collectors.

## Slide 15: Average Speed by Functional Class
Chart: 5th Percentile Average Speed by Functional Class
| 10 | 20 | 40 | 60 | 70 | 90
AM speed | 53 | 46 | 28 | 20 | 44 | 48
Midday speed | 56 | 45 | 28 | 19 | 46 | 51
PM speed | 51 | 45 | 27 | 19 | 45 | 45
Evening speed | 57 | 46 | 28 | 20 | 47 | 52
Night speed | 59 | 46 | 30 | 20 | 46 | 55

## Slide 18: Average Speed by Area Type
50 percentile speed
  TOD
    AM Peak (6AM – 9AM)
    Midday (9AM – 3PM)
    PM Peak (3PM – 7PM)
    Evening (7PM – 10PM)
    Night (10PM – 6AM)
  ATG
    1  CBD
    2  Fringe
    3  OBD
    4  Generally Residential
    5  Rural
Notes: Average speed increases from CBD to Rural for roadways of all facility types

## Slide 19: Average Speed by Area Type
Chart: 50th Percentile Average Speed by Area Type
AM speed | 27.7581 | 30.3181 | 30.361 | 34.0509 | 44.4902
Midday speed | 26.6835 | 29.2872 | 30.0317 | 33.5478 | 44.048
PM speed | 25.2592 | 25.7448 | 27.9633 | 32.5114 | 44.5992
Evening speed | 27.7815 | 31.2368 | 31.6735 | 34.7136 | 45.1136
Night speed | 29.6934 | 35.1364 | 34.7029 | 36.9715 | 46.1126

## Slide 20: Average Speed by Functional Class
5 and 50 percentile speed
  FTC*
    10  Freeway
    20  Uninterrupted Facility
    40  Higher Speed Interrupted Facility
    60  Lower Speed & Collector Facility
    70  Ramps
    90 Toll Roads
Notes: As shown in the blue rectangular, AM, PM and Midday average speed are quite similar for arterials and collectors.

## Slide 21: Average Speed by Functional Class
Chart: 50th Percentile Average Speed by Functional Class
| 10 | 20 | 40 | 60 | 70 | 90
AM speed | 54 | 47 | 29 | 22 | 44 | 49
Midday speed | 56 | 46 | 28 | 20 | 46 | 52
PM speed | 52 | 47 | 27 | 20 | 46 | 46
Evening speed | 58 | 48 | 30 | 21 | 48 | 53
Night speed | 60 | 47 | 32 | 22 | 48 | 56
*80-HOV is not included because 24-hr count for HOV is not available.

## Slide 24: Discussion
Midday speed is as congested as AM speed for arterials and collectors
Notes: http://www.fsutmsonline.net/images/uploads/md_lctr_2006/SERPM7_Model_Development_Report_Feb_17_2015_Final.pdf
*Only 11% of workers above 16 leaving home from 10 am to 4 pm for county-to-county flow according to CTPP 2006-2010 data
*That number for MWCOG region is about 8%
  More non-mandatory tours than other region?
  More flexible work schedule in this region?* (not likely)
  Departure or arrival times at noon for university & school tours?
Comparing Arterial Speeds from “Big-Data” Sources in Southeast Florida (Abstract) (Presentation)Presented by Sujith Rapolu
Authors: Sujith Rapolu, AECOM Ashutosh Kumar, AECOM

## Slide 25: Discussion
Comparing Arterial Speeds from “Big-Data” Sources in Southeast Florida (Rapolu & Kumar, 2015)
  Midday speed is as slow as AM speed
  Congested Speed is approximately half of the posted speed limit
  PM speed is the slowest
Chart: NPMRDS Arterials
| AM Speed | Midday Speed | PM Speed | Evening Speed | Nightime Speed | Peak Speed | Off-peak Speed | Daily Speed | Average Posted Speed
 | 28.4694 | 27.6282 | 26.7589 | 28.4695 | 30.2082 | 27.4741 | 28.1727 | 27.8589 | 42.1468
NPMRDS data for Higher Speed Interrupted Facility
is almost consistent with the previous study conducted in 2015 .
Notes: Comparing Arterial Speeds from “Big-Data” Sources in Southeast Florida (Abstract) (Presentation)Presented by Sujith Rapolu
Authors: Sujith Rapolu, AECOM Ashutosh Kumar, AECOM

## Slide 26: Discussion
Chart: NPMRDS Weighted Daily Average Speed
| 10 | 20 | 40 | 60 | 70 | 90
5th Daily Speed | 55 | 45 | 28 | 20 | 45 | 49
50th Daily Speed | 55 | 47 | 29 | 21 | 46 | 50
Comparing Arterial Speeds from “Big-Data” Sources in Southeast Florida (Rapolu & Kumar, 2015)
  Average travel speed during the day is 20-25 mph for the four major corridors
NPMRDS daily weighted congested speed is a bit higher than data in this previous study.
Notes: Weighted 5th daily speed for arterial is a bit higher compared to major arterials because speed of roadways in rural area is also included.
Comparing Arterial Speeds from “Big-Data” Sources in Southeast Florida (Abstract) (Presentation)Presented by Sujith Rapolu
Authors: Sujith Rapolu, AECOM Ashutosh Kumar, AECOM

## Slide 27: SERPM 6 – Speed Validation
 |  | Average Weighted Speed (mph) |  |  |  |  |  |  | 
 |  | Model |  |  |  | Observed |  |  | 
Facility Type |  | AM | PM | Off Peak | All Periods | AM | PM | Off Peak | All Periods
Freeway - | 11 | 45.41 | 45.47 | 48.81 | 46.44 | 46.84 | 54.15 | 52.25 | 50.58
Surface Streets - | 41 | 29.86 | 27.45 | 31.67 | 30.13 | 24.69 | 23.60 | 26.62 | 25.25
HOV Lanes - | 81 | 54.02 | 51.57 |  | 52.79 | 64.19 | 57.58 |  | 60.89
Toll Facility - | 91 | 63.79 | 62.17 | 62.84 | 62.96 | 65.16 | 65.47 | 63.97 | 65.17
All Facilities: |  | 41.00 | 43.94 | 37.87 | 40.88 | 39.97 | 46.75 | 35.41 | 40.48
Data Source: Li, S, et al. (2007). Validation of Speeds and Capacities in a Large Regional Model. Page 23. http://www.trbappcon.org/2007conf/program.html#s16a
Notes: 54 mph for NPMRDS AM looks a bit high compared with 2000 freeway speed (46.84 mph) shown in the table of this slide
28 mph for NPMRDS AM looks a bit high compared with 2000 freeway speed (24.69 mph) shown in the table of this slide
Data source of observed speed looks like an inventory maintained by FDOT

## Slide 28: Average Speed by Functional Class
5 percentile speed
  FTC*
    10  Freeway
    20  Uninterrupted Facility
    40  Higher Speed Interrupted Facility
    60  Lower Speed & Collector Facility
    70  Ramps
    90 Toll Roads
*80-HOV is not included because 24-hr count for HOV is not available.
Data Source: HERE
with high confidence (>0.7))
Chart: HERE 5th Percentile Average Speed
| 10 | 20 | 40 | 60 | 70 | 90
AM Speed | 43 | 45 | 25 | 19 | 39 | 34
Midday Speed | 50 | 44 | 25 | 17 | 41 | 40
PM Speed | 43 | 45 | 24 | 17 | 42 | 37
Evening Speed | 55 | 47 | 29 | 20 | 44 | 45
Night Speed | 56 | 49 | 33 | 24 | 43 | 46
Here data has freeway and arterial AM speed more consistent with 2000 highway speed
Notes: Here data has freeway and arterial AM speed more consistent with 2000 highway speed

## Slide 29: Free-flow Speed Derivation
FTC2 | Functions
11-12, 81-82, 91-92 | FFSPD=12.56418+0.64058*POSTSPD+0.00340*(POSTSPD)^2
21,41,61 | FFSPD=10.10+0.65735*POSTSPD+0.00348*(POSTSPD)^2
71-75, 83-86, 93-95 | FFSPD=11.33209+0.64896*POSTSPD+0.00344*(POSTSPD)^2
*Based on SERPM 7 CUBE script, free-flow speed is derived based on posted speed.
Notes: IF (FTC2=11-12,81-82) ;Freeway & HOV
FFSPD=(12.56418+0.64058*POSTSPD+0.00340*(POSTSPD)^2)
ELSEIF (FTC2=91-92) ;Mainline Toll Links
FFSPD=(12.56418+0.64058*POSTSPD+0.00340*(POSTSPD)^2)
ELSEIF (FTC2=21) ;Uninterrupted Roadways
FFSPD=(10.10+0.65735*POSTSPD+0.00348*(POSTSPD)^2)
ELSEIF (FTC2=41) ;High Speed Arterials
FFSPD=(10.10+0.65735*POSTSPD+0.00348*(POSTSPD)^2)
ELSEIF (FTC2=61) ;Low Speed Collectors
FFSPD=(10.10+0.65735*POSTSPD+0.00348*(POSTSPD)^2)
ELSEIF (FTC2=71-75) ;Ramps-Freeway
FFSPD=(11.33209+0.64896*POSTSPD+0.00344*(POSTSPD)^2)
ELSEIF (FTC2=93,94) ;Ramps-Toll Facilities
FFSPD=(11.33209+0.64896*POSTSPD+0.00344*(POSTSPD)^2)
ELSEIF (FTC2=83-86) ;HOV Slip Ramps
FFSPD=(11.33209+0.64896*POSTSPD+0.00344*(POSTSPD)^2)
ELSE
FFSPD=(11.33209+0.64896*POSTSPD+0.00344*(POSTSPD)^2) ;Others (for ex. Toll plazas-95) excluding connectors
ENDIF

## Slide 30: Reference, Free-flow & Posted Speed Cont’d.
Chart: Average Reference Speed, Free-flow Speed & Posted Speed
| CBD | Fringe | OBD | Generally Residential | Rural | Fringe | OBD | Generally Residential | Rural | CBD | Fringe | OBD | Generally Residential | Rural | CBD | Fringe | OBD | Generally Residential | Fringe | OBD | Generally Residential | Fringe | OBD | Generally Residential | Rural | Freeway | Uninterrupted Facility | Higher Speed Interrupted Facility | Lower Speed &Collector Facility | Ramps | Toll Roads
Reference Speed | 55 | 55.6098 | 60.5294 | 63.8 | 66.25 | 45 | 45 | 47.4138 | 52.2727 | 27.5 | 30.0685 | 33.0056 | 37.807 | 46.3636 | 17.7273 | 27.037 | 27.6389 | 31 | 45 | 45 | 49.6154 | 60 | 56.5278 | 58.8211 | 57
Free-flow Speed | 53.6316 | 53.6853 | 59.3112 | 64.9142 | 71.9314 | 53.0901 | 57.0468 | 52.0254 | 57.9375 | 30.736 | 32.9234 | 34.3888 | 37.695 | 41.1398 | 26.5497 | 29.4868 | 31.4434 | 33.3055 | 49.4025 | 49.0998 | 49.6932 | 52.0909 | 48.6107 | 48.3994 | 46.3162
Posted Speed | 55 | 55 | 59.6037 | 64.5286 | 70 | 52.1429 | 55.5263 | 52.9365 | 57.2703 | 35.3065 | 38.7452 | 39.2896 | 41.2562 | 41.2 | 28.3815 | 31.1574 | 31.714 | 32.378 | 46.8046 | 46.4875 | 47.0057 | 49.2857 | 45.9865 | 45.3558 | 43.0769
Data source:
1) Reference speed: NPMRDS one-hour 85th percentile average speed for each link attached with a valid TMC
2) Free-flow and posted speed: SEPRM 7 loaded network
Notes: Not sure if the reference speed a bit low to uninterrupted facilities in urban area.
Data source:
1) Reference speed: NPMRDS one-hour 85th percentile average speed for each link attached with a valid TMC
2) Free-flow and posted speed: SEPRM 7 loaded network
Reference speed is too low for Lower Speed & Collector Facility in CBD

## Slide 31: Discussion
For categories with counts greater than 20, most of free-flow speed calculated in the loaded network is between posted speed and reference speed, which is consistent with SERPM 7 summary in the model development report

## Slide 32: Conclusion
Average speeds for different time periods are consistent with other sources
Reference speed calculated by 85 percentile daily speed has logical relationship with post speed and free flow speed