## Slide 1: Origin / Destination Sources
presented by Daniel R. Miller, P.E. September 1st, 2020

## Slide 2: Overview
Data Source
  Data Provider
  Data Type
  Committee Comments
  Source

## Slide 3: Commercial
Streetlight
Cell-phone / GPS based
  Inrix, Siemens, Forum Analytics, Iteris
  Saas platform
Notes:
  Pretty good, accomplished Richmond TAZ extraction, has been to TMC OD level
  Most satisfied
AirSage
Cell-Phone / GPS based
  Saas platform
Comments
  Used for Kentucky Validation
  Concerns over Data
  Found that the raw data could not be used, procured data and had to produce a factor. Data was good for trip frequency.
  AirSage has an option for trucks as one purchase;

## Slide 4: Commercial
License Plate Survey
On-Site Survey: Photo/Video
  Capture license plates at locations and O-D paths
Read License Plate and match with DMV
Comments:
  Reliable
  Only deals with limited areas
  Public pushback on how acquired
  OCR will output regardless of validity
Helicopter / Drone (SkyComp)
On-Site Survey:
  Video of vehicles and develop O-D paths
Track vehicles within camera field
  Possible to piece together larger area using multiple drones
Comments:
  Skycomp: Study in Bronx, limited study area, high speed aerials, track individual vehicles. Very expensive. Provide an O-D Matrix with file of aerials.
  Research looks to be going to drones

## Slide 5: Commercial
American Transportation Research Institute
Data Set
  Processed truck GPS data
  Data only from companies that volunteer to share
Comments:
  Study for Polk TPO. Provides a select link assignment that provides volumes (trucks only)
  ATRI data is very good,
  Matrix data was expanded to rural parts of trucking industry
IHS Tourism Data
Data Set
  Metropolitan Statistical Area Level
  Survey of IHS members
Comments:
  Good for national data to Florida
  Need to disaggregate data

## Slide 6: Commercial
Uber Movement
Data Set
  Travel Times by period
    Highly customizable
  Urban Cities
  Free to download
Comments:
  Limited to cities with enough data
  No volumes
Moonshadow / WeJo
Data Set
  Inrix Trip Paths
    GPS data
  Organizes to DB4IoT
Comments:
  Not familiar with them
  Inrix Trip Analytics is another data source to look at

## Slide 7: Commercial
Bluetooth
Data:
  Collected from Bluetooth MAC addresses that are open
  Needs collection spots
Comment:
  Low capture rates
  MioVision at the ports, set there to identify trucks with bluetooth across the state. Good for long distance capture.
Strava
Data:
  Pulls from Runners and Cyclists
Comment:
  Department has the data

## Slide 8: Commercial
InfoGroup
Data:
  Parcel data and in-depth data to differentiate populations in TAZ
Comment:
  Identify methods for destination
    LinkedIn
Credit Card Data
Data:
  Provides credit card purchase locations
Comment:
  Provides possible trip chains
  Not capable of identifying origin

## Slide 9: Government
Travel Diary
Data Set
  Contact individuals
  Collect and organize data
Comments:
  Done all over the country, now done via phone surveys, becoming more difficult as individuals go to cell phones. Samples have been adjusted to be based from Post Office addresses.
  Infogroup to get addresses, but having difficulties getting respondents to paper survey.
  Has been done via phone app, tracks via GPS, battery issue
  User engagement
National Household Travel Survey
Data Set:
  2009 NHTS (Travel Diary Based)
  2017 is available but not a lot of data points from Florida
Comments:
  Even with 2009 sample still felt we needed more

## Slide 10: Government
Longitudinal Employer-Household Dynamics
Data:
  Employment Statistics
  2002 – 2017
  Census Blocks
Comment:
Freight Analysis Framework
Data:
  Access database with future forecasts from 2020 to 2045
  Tonnage, value, and ton-miles by region
Comment:
  Broken down to lower levels using TranSearch data

## Slide 11: Government
Department of Motor Vehicles
Data Set:
  Difficult to get access
Weigh in Motion Stations
Comment:
  Single point information, no O-D data
  Ed Hutchinson is working to capture taxonomy for the trucks

## Slide 12: Government
Video Camera’s on Site
Data:
  In-situ cameras
  OCR of license plate between cameras
Comment:
  Proposed with app, Waze, to find origins / destinations
  Private industry may implement something similar
Sunpass / E-Pass
Data:
  Transponder O-D’s
  Off-system items
Comment:
  Very difficult to get the data

## Slide 13: Social Media
Four Square
Data:
  Older data is available for download
Comment:
  Not officially released
Twitter
Data:
  GPS data on images
  Hashtags provide general information
Comment:
  Use the twitter pipe to organize data
  Concern for socio-economic bias
  Better in high density areas

## Slide 14: Social Media
Instagram / Facebook
Data:
  API is available
Comment:
  Facebook is difficult to access the API to pull data from
LinkedIn
Data:
  Work site
Comment:
  Scrape of LinkedIn data to pair with available parcel data for general O-Ds

## Slide 15
Questions?