## Slide 1: Florida Statewide Model Strategic Intermodal System Prioritization and Integration
Presented by
Jeanette Berk and Hoyt Davis

## Slide 2
Supplement to the SIS Work Program Process
  Provide backcheck for the current project ranking process
    Generate Measures of Effectiveness (MOE) Reporting
  Geographical representation of SIS Work Program projects associated with travel demand estimates
    Plots of Network Differences
    Plots of Model Volumes
  Analysis of Project Phasing
    Definition of project phasing
FLSWM – SIS Prioritization and Integration
Goal of Project

## Slide 3
FLSWM Master Network
Network used for statewide traffic forecasts
Does have True Shape shapefile
SIS Shapefile
Inventory of SIS facilities and future year plans
RCI
Data
Maintained inventory of all State and Federal roadway Systems
FLSWM – SIS Prioritization and Integration
Data
Sources

## Slide 4
FLSWM – SIS Prioritization and Integration
Create network and attributes from RCI
  RCI database
  Network elements
  Expand RCI data
Refine network directionality and characteristics
  Facility types and centroid connections
  True shape structure
Create additional tools
  Centroids and connectors
  Other FLSWM attributes
Methodology

## Slide 5
FLSWM – SIS Prioritization and Integration
Network Creation Automation Process

## Slide 6
RCI Base Map Automation to Model Network
#1 Select RCI Basemap Arcs
Demo tool was developed to sub-select RCI Basemap Routes and Arcs by County
  Demo used Hernando & Citrus Counties were selected
  Current tool is Statewide for SIS network development
Citrus
Hernando
Citrus
Hernando

## Slide 7
RCI Base Map Automation to Model Network
#2 Create RCI Arc Nodes
To create node features for Basemap arc identification
  Redundant nodes are removed
Preserves RCI Basemap intersections, measures and other points of connectivity
#3 Route 800 Series to Route
To analyze RCI route relationships in GIS to better process divided roadways and their reverse traffic flow routes and attributes

## Slide 8
RCI Base Map Automation to Model Network
8
#4 Create RCI Arc Events
Basemap Arcs
  Unique node (ANODE - BNODE) pairs added to each arc
New Arcs RCI Event Table
  Arcs layer exported to table with RCI linear reference
#5 Update/Capture 800 RCI Arc Events
Process relationships of reverse traffic flow routes attributes of divided roadways

## Slide 9
RCI Base Map Automation to Model Network
#6 Capture RCI Attribute Events Tables
Initial Attributes
  SIS
  Functional Classification
  Number of Lanes
  Max Speed
  Road Type
Additional attributes
  Count Stations
    TTMS
    PTMS
  Signal locations
  Turn-lanes
  SIS Cost Feasible and Needs Plans

## Slide 10
RCI Base Map Automation to Model Network
#8 Manipulate RCI Layer
Make graphic adjustments for a combined model network layer
  Maintain “True” shape GIS characteristics
  Change “C”-Composite link attributes
  Add break points for centroid link connectors
  Adjust directionality
  Add back in GIS based network connectors without RCI attributes
#7 Reverse 800 RCI Arc Events
Assign reverse traffic-flow attributes for use on the RCI “800” routes which represents the opposite-side of divided roadway facilities
  RCI uses side attribute types L, R, & C for distinction of side-of-road

## Slide 11
RCI Base Map Automation to Model Network
Example of Graphical Changes
Change “C”-Composite link information to directional
Adjust Arcs directionality
Attributes Layer w/ RCI Directional Arcs
Attributes Layer w/ RCI Directional Arcs (offset for clarity)
Attributes Layer w/Reverse Directional Arcs (offset for clarity)
14

## Slide 12
RCI Base Map Automation to Model Network
#9 Create RCI Attribute Nodes
Create a final node structure / nodes layer for the new combined model links layer with RCI attributes
#10 Create RCI Nodes on Layer
To relate the new node structure back to the combined model links layer with RCI attributes

## Slide 13
RCI Base Map Automation to Model Network
#11 Update Connectors
To extend RCI attributes to network connectors from their neighboring links
RCI Arc Connectors shown in Pink are not part of RCI Attributes
Arc Connectors are added to Travel Demand Model network layer and given adjacent link Attributes

## Slide 14
RCI Base Map Automation to Model Network
Other Tool Development
Add centroids and centroid connectors to RCI model links to be use for FLSWM network
Add any other attribution used by the FLSWM for reporting
Add new attributes to represent the future SIS network changes
  SIS Cost Feasible Plan
  SIS Needs Plan

## Slide 15
RCI Base Map Automation to Model Network
Build master model network
Run model alternatives
Compare SIS model runs
FLSWM Application
Current Year
Cost Feasible Plan
Needs Plan

## Slide 16
Contact Infomration
Terrence Corkery
Terrence.Corkery@dot.state.fl.us
Jeanette Berk
jberk@gfnet.com
Hoyt Davis
hdavis@gfnet.com
Thank You!
Questions